## Slide 1: Robust train routing in station areas with reducing capacity utilization
Rotterdam, 20-07-2015
CASPT 2015
Nikola Bešinović, Rob M.P. Goverde
The 13th Conference on Advanced Systems in Public Transport

## Slide 2: Outline
Introduction
Motivation
Solution approach
  Preprocessing
  Original Train Routing Problem (TRP)
  Extension to Robust Train Routing Problem (RTRP)
  RTRP heuristics
Case study
Introduction | Motivation | Methodology | Case study | Discussion

## Slide 3: Introduction
High capacity consumption (sometimes over recommended norms)
Growing demand (e.g., NL - a train every 5’)
Stations as bottlenecks
New planning methods and algorithms that should provide:
  High-quality and reliable service,
  Improved experience for planners and dispatchers
  Satisfied customers
Train routing problem: 1. platform assignment
2. route selection
Introduction | Motivation | Methodology | Case study | Discussion

## Slide 4: State-of-the-art of Train Routing Problem (TRP)
TRP is NP-hard
So far: Sels et al. (2014), Cacchiani et al. (2014)
  Aggregated routes
  Only platforming
  Node/set packing
  Conflict graph
  Multi-commodity flow
  Fixed/flexible event times
Still missing:
  Not proven operational feasibility
  Infrastructure occupation and maintenance not considered
Introduction | Motivation | Methodology | Case study | Discussion

## Slide 5: Robust train routing problem (RTRP)
Problem:
Find the feasible, stable and robust route plan (RP), i.e., platform allocation and routing, that uses the infrastructure more evenly within a station area
Input:
  Station topology
  Train lines
  Set of alternative routes
  Fixed event times (arrivals and departures) – output from a macroscopic timetabling model
  Preferred platforms for train lines
  Passenger connections
Introduction | Motivation | Methodology | Case study | Discussion

## Slide 6: Some definitions
Station topology – detailed infrastructure
Resource – subset of infrastructure elements
  Track section, switch, crossing
A train route – set of resources
Blocking time – a time that a resource is reserved exclusively for a single train
Blocking time > running time over a resource
Introduction | Motivation | Methodology | Case study | Discussion

## Slide 7
Introduction | Motivation | Methodology | Case study | Discussion
Introduction
Motivation
Solution approach
  Preprocessing
  TRP model
  RTRP model
  RTRP heuristics
Case study
Building a graph…
Resource trees
Blocking times
Conflict constraints

## Slide 8: Preprocessing (1)
Introduction | Motivation | Methodology | Case study | Discussion
Resource tree – acyclic graph that includes all alternative routes
Resource trees
Blocking times
Conflict constraints

## Slide 9: Preprocessing (1)
Introduction | Motivation | Methodology | Case study | Discussion
Resource tree – acyclic graph that includes all alternative routes
Resource trees
Blocking times
Conflict constraints

## Slide 10: Preprocessing (1)
Introduction | Motivation | Methodology | Case study | Discussion
Resource tree – acyclic graph that includes all alternative routes
Resource trees
Blocking times
Conflict constraints

## Slide 11: Preprocessing (2)
Introduction | Motivation | Methodology | Case study | Discussion
Time
Resource trees
Blocking times
Conflict constraints

## Slide 12: Preprocessing (2)
Introduction | Motivation | Methodology | Case study | Discussion
Time
Resource trees
Blocking times
Conflict constraints

## Slide 13: Preprocessing (3)
Introduction | Motivation | Methodology | Case study | Discussion
Resource trees
Blocking times
Conflict constraints

## Slide 14: Preprocessing (3)
Introduction | Motivation | Methodology | Case study | Discussion
Conflict arcs:
Resource trees
Blocking times
Conflict constraints

## Slide 15
Introduction | Motivation | Methodology | Case study | Discussion
Introduction
Motivation
Solution approach
  Preprocessing
  TRP model
  RTRP model
  RTRP heuristics
Case study

## Slide 16: TRP model
Multi-commodity flow problem
Train = commodity
Objective
  Max quality of chosen routes
  (short running times)
Constraints
  Capacity constraints
  Flow conservation
  Conflict constraints
Caimi (2009)
Introduction | Motivation | Methodology | Case study | Discussion

## Slide 17
Introduction | Motivation | Methodology | Case study | Discussion
Introduction
Motivation
Solution approach
  Preprocessing
  TRP model
  RTRP model
  RTRP heuristics
Case study

## Slide 18: RTRP model
Extension of TRP model 1. robustness
2. capacity occupation
Robustness = increase buffers between train routes (Caprara et al. 2011)
For two train routes
Buffer costs are assigned between leaves of resource trees
Introduction | Motivation | Methodology | Case study | Discussion

## Slide 19: RTRP model
Capacity occupation is a summation of critical processes as minimum headways, scheduled running or dwell times
Capacity occupation = critical (longest) path over chosen routes
Lower capacity occupation provides more time allowances
(i.e., better stability)
To evaluate capacity occupation minimum headways are needed
Add arcs with weights that correspond to minimum headways
Introduction | Motivation | Methodology | Case study | Discussion

## Slide 20: RTRP model
Headway arcs
Computed based on blocking times
Introduction | Motivation | Methodology | Case study | Discussion

## Slide 21: RTRP model
Headway arcs
Add source and sink nodes
Introduction | Motivation | Methodology | Case study | Discussion

## Slide 22: RTRP model
Active headways depend on selected routes
Active headway arcs
Introduction | Motivation | Methodology | Case study | Discussion

## Slide 23: RTRP model
Introduction | Motivation | Methodology | Case study | Discussion
Active headways depend on selected routes
Active headway arcs
Directed acyclic graph
Find the critical path
Adjusted LP formulation for shortest path problem

## Slide 24: RTRP model
Introduction | Motivation | Methodology | Case study | Discussion
Objectives
  Max quality of chosen routes
  Max robustness
  Min capacity occupation (critical path)
Constraints
  Capacity constraints
  Flow conversation
  Conflict constraints
  Active headways
  Shortest path constraints
  Maximum permitted capacity occupation
Developed heuristics for solving RTRP

## Slide 25
Introduction | Motivation | Methodology | Case study | Discussion
Introduction
Motivation
Solution approach
  Preprocessing
  TRP model
  RTRP model
  RTRP heuristics
Case study

## Slide 26: RTRP heuristics
Introduction | Motivation | Methodology | Case study | Discussion
Local search algorithm
Main components
  Capacity assessment (CA)
  Robustness evaluation (RE)
  Improvement rules (IR)
Algorithm of the RTRP heuristics
  Input: route plan
  Initialize
  While OR
  Compute capacity occupation CA
  Compute delay propagation RE
  if <
  end if
  vary routes in (IR)
  End while

## Slide 27: RTRP heuristics
Introduction | Motivation | Methodology | Case study | Discussion
Capacity assessment
  Compression method (UIC 406)
  Microscopic model
  Algebraic approach = Max-plus automaton
  All train dependencies naturally considered
  Output: capacity occupation, resources at the critical path, occupation of each resource
Robustness evaluation
  Delay propagation model
  Input: set of delay realisations
  Output: average delay

## Slide 28: Methodology
Substitute bad train routes
Exclusion (E) and inclusion (I) rules for alternating routes in the route plan
E-rules. Choose a route that:
  has a resource is on the critical path
  uses a platform with the highest occupation
  generates the most delays
I-rules. Choose a route that:
  Does not use a resource on a critical path
  Does not use the highest utilised platform
  Is not conflicting with existing routes in the route plan
Route permutations
Introduction | Motivation | Methodology | Case study | Discussion

## Slide 29
Introduction | Motivation | Methodology | Case study | Discussion
Introduction
Motivation
Solution approach
  Preprocessing
  TRP model
  RTRP model
  RTRP heuristics
Case study

## Slide 30: Case study
Introduction | Motivation | Methodology | Case study | Discussion
Period (s) | 1800
# of platforms | 6
# of routes | 91
maxIter | 500
convIter (iterations without improvement) | 100
Table 1. Input parameters
Station Den Bosch
14 trains lines with periodicity of 2 trains/h
Input: computed timetable
Besinovic et al. 2015

## Slide 31: Case study
Introduction | Motivation | Methodology | Case study | Discussion
Parameters | Mean (s) | Standard deviation (%)
Total cost (s) | 1135 | 0.73
# of iterations | 165 | 34.57
Table 1. Heuristics convergence
Initial results
Heuristics performance
30 repeated runs of RTRP heuristics
Weights for CA and RE are equal

## Slide 32: Case study
Introduction | Motivation | Methodology | Case study | Discussion
Initial results
 | Capacity occupation (s) | Average delay (s) | Total cost (s) | Number of resources used
Only CA | 801 | 796 | 1597 | 72
Only RE | 956 | 301 | 1257 | 58
CA & RE | 821 | 314 | 1135 | 70
Table 2. Results of individual submodels
Test single submodels CA and RE vs CA+RE
CA = original TRP

## Slide 33: Conclusion
Introduction | Motivation | Methodology | Case study | Discussion
New multiobjective MILP formulation for robust train routing problem
Promising heuristics for solving RTRP
Optimized route plan fulfils
  Proven feasibility (at microscopic level)
  Capacity consumption reduced
  Improved robustness
  More even resource usage => less frequent maintenance
Future work
  Compare results with the optimal solution
  Flexible event times
  Evaluate the effect of different weights for CA and RE

## Slide 34
Thank you for your kind attention
n.besinovic@tudelft.nl

## Slide 35: References
Sels P., Vansteenwegen P., Dewilde T., Cattrysse D., Waquet B., Joubert A., The train platforming problem: The infrastructure management company perspective, Transportation Research Part B: Methodological, Volume 61, March 2014, pp. 55-72
Besinovic N., Quaglietta E., Goverde R.M.P., A simulation-based optimization approach for the calibration of dynamic train speed profiles, Journal of Rail Transport Planning and Management, Journal of Rail Transport Planning & Management, Volume 3, Issue 4, 2013, pp. 126–136
Hansen I.A., Pachl J., Railway Timetable and Traffic, Eurailpress, Hamburg, Germany, 2008.
Viennot G.X., Heaps of pieces I: Basic definitions and combinatorial lemmas, lecture notes in mathematics, 1234,
Egmond R.J., An algebraic approach for scheduling train movements, The 8th International Conference on Computer-Aided Scheduling of Public Transport (CASPT 2000), Berlin, 21-23 June, 2000.
Goverde, R.M.P., Railway Timetable Stability Analysis Using Max-Plus Sys-tem Theory. Transportation Research Part B, 41(2), 179-201, 2007.
UIC Code 406: Capacity. International Union of Railways, Paris, 2nd Edition, June 2012.
Sparing D., Goverde R.M.P., An Optimization Model for Periodic Timetable Generation with Dynamic Frequencies, 16th International IEEE Conference on Intelligent Transport Systems (IEEE ITSC 2013), 6-9 October, The Hague, 2013.
Gaubert, S. and Mairesse, J., “Modeling and Analysis of Timed Petri Nets using Heaps of Pieces”, IEEE Transactions on Automatic Control, vol. 44, no. 4, pp. 683–697, 1999.

## Slide 36: Case study
Introduction | Motivation | Framework | Methodology | Case study | Discussion
Optimized route plan
*red train route is repeated from the next period

## Slide 37: Train routing problem (TRP)
Introduction | Motivation | Methodology | Case study | Discussion
Platform utilization

## Slide 38: Train routing problem (TRP)
Utrecht Central
Introduction | Motivation | Methodology | Case study | Discussion
Routing possibilities

## Slide 39: Introduction
Feasibility -The ability of all trains to adhere to their scheduled train paths
Stability -The ability of a timetable to absorb initial and primary delays so that delayed trains return to their scheduled train paths without rescheduling.
Robustness -The ability of a timetable to withstand design errors, parameter variations, and changing operational conditions.
Resilience - The flexibility of a timetable to prevent or reduce secondary delays using rescheduling measures (re-timing, re-ordering, re-routing).
Some definitions
Introduction | Motivation | Methodology | Case study | Discussion
Deliverable D3.1 (ONTIME, 2013)
  Realisable
  Conflict-free

## Slide 40: Preprocessing – Route reduction
Introduction | Motivation | Methodology | Case study | Discussion
Zwaneveld et al. (1996)
De Wilde et al. (2014)

## Slide 41: Preprocessing
Blocking time block i of train j
Blocking time computation
Introduction | Motivation | Methodology | Case study | Discussion